## Slide 1
BUILDING FAÇADE LAYOUTS AND OPTIMIZATION
Final Project | 5002 Discrete Structures | Lipeipei Sun

## Slide 4: BASIC BUILDING FAÇADE REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet.
54’
140’

## Slide 5: BASIC BUILDING FAÇADE REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet.
(40” X 42BAYS)
54’
18’
18’
15’
3’
140’

## Slide 6: BASIC BUILDING FAÇADE REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet
(40” X 42BAYS)
54’
18’
18’
15’
3’
140’

## Slide 7: BASIC BUILDING FAÇADE REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet
(40” X 42BAYS)
54’
18’
18’
15’
3’
EL0
EL15
EL33
140’
12’
15’
15’

## Slide 8: PERFORMANCE REQUIREMENTS
The total glazing (window area) should be between 35% to 40% of the total facade area for each level.
Glazing area / Total area
Windows to be evenly distributed.

## Slide 9: AESTHETIC PREFERENCES
Preference for 6 feet and 9 feet panels.
The 3 feet panel should be used between two windows.
No more than two windows should be adjacent to each other to maintain the building's aesthetic integrity.
9’ panel
6’ panel
3’ panel

## Slide 10: PROCESS
54’
(40” X 42 BAYS)
140’
STEP 1.
Find all valid options for the vertical bays
STEP 2.
Rearrange the vertical bays on building façade based on the requirements

## Slide 11: OTPIONS FOR VERTICAL BAYS
BUILDING HEIGHT
(54 FOOT MAX)
141 OPTIONS
(REPRESENTED AT 40” WIDE PER BAY)
Combinations based on
3’, 6’, 9’ solid panels
12’ and 15’ windows

## Slide 12: NARROW DOWN THE OPTIONS
BUILDING HEIGHT
(54 FOOT MAX)
141 OPTIONS
(REPRESENTED AT 40” WIDE PER BAY)
Eliminate invalid options
Max two 3’ panel unless there is a window
Max one 12’ tall window and two 15’ tall window

## Slide 13: NARROW DOWN THE OPTIONS
BUILDING HEIGHT
(54 FOOT MAX)
15 OPTIONS
Eliminate invalid options
Max two 3’ panel unless there is a window
Max one 12’ tall window and two 15’ tall window
141 OPTIONS
BUILDING HEIGHT
(54 FOOT MAX)

## Slide 14: Permutations
BUILDING HEIGHT
(54 FOOT MAX)
15 OPTIONS
PANEL TYPES
28 WAYS TO ARRANGE
THE PANELS
Get valid and unique panel arrangements

## Slide 15: Permutations
BUILDING HEIGHT
(54 FOOT MAX)
15 OPTIONS
6 PANEL TYPES
Get valid and unique panel arrangements
12’ window
6’ panel
3’ panel
9’ panel
15’ window
9’ panel
6!
2!
= 360

## Slide 16
6 PANEL TYPES
360 OPTIONS

## Slide 17: Permutations
6 PANEL TYPES
3 WAYS TO
ARRANGE THE PANELS
Get valid and unique panel arrangements
Ensure windows are located at the correct height
EL0
EL15
12’
15’
BUILDING HEIGHT
(54 FOOT MAX)
15 OPTIONS

## Slide 18: Permutations
Get valid and unique panel arrangements
BUILDING HEIGHT
(54 FOOT MAX)
15 OPTIONS
113 OPTIONS

## Slide 19: Permutation (113, 42)
113 valid options SELECT 42 vertical bays
(40” X 42 BAYS)
54’
140’

## Slide 20: REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet (42 Bays)
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet
The total glazing (window area) should be between 35% to 40% of the total facade area for each level.
Windows to be evenly distributed.
Preference for 6 feet and 9 feet panels.
The 3 feet panel should be used between two windows.
No more than two windows should be adjacent to each other to maintain the building's aesthetic integrity.
BASIC DIMENSIONS
PERFORMANCE
AESTHETIC

## Slide 21: REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet (42 Bays)
  Height: 54 feet
Building Stories:
  Story height:
  15 feet at Level 1
  18 feet at Level 2 and 3
  3 feet at parapet
  Total stories: 3
Panel Sizes:
  Heights: 3, 6, or 9 feet
  Width: 40 inches (10/3 feet)
Window Specifications:
  Height:
  12 feet at Level 1
  15 feet at Level 2 and 3.
  Located at floor level with elevations:
  0, 15, and 33 feet
The total glazing (window area) should be between 35% to 40% of the total facade area for each level.
Windows to be evenly distributed.
Preference for 6 feet and 9 feet panels.
The 3 feet panel should be used between two windows.
No more than two windows should be adjacent to each other to maintain the building's aesthetic integrity.
BASIC DIMENSIONS
PERFORMANCE
AESTHETIC

## Slide 22
113 select 42 with repetitions
=
113^42
113 select 42 without repetitions
=
113! / (113-42)!

## Slide 23: REQUIREMENTS
Building Facade Dimensions:
  Width: 140 feet (42 Bays)
The total glazing (window area) should be between 35% to 40% of the total facade area for each level.
Windows to be evenly distributed.
No more than two windows should be adjacent to each other to maintain the building's aesthetic integrity.
BASIC DIMENSIONS
PERFORMANCE
AESTHETIC

## Slide 24: METHOD 1 - Simplifying the Combination Analysis & Finding Patterns
(40” X 42 BAYS)
54’
140’

## Slide 25: PERFORMANCE
42 VERTICAL BAYS
19 - 21 WINDOWS
18 – 20 WINDOWS
18 – 20 WINDOWS
882sf to 1008sf
2520sf
Glazing area
Total area
882sf to 1008sf
2520sf
735sf to 840sf
2100sf
# of windows required
= 35% - 40%
LEVEL 3
LEVEL 2
LEVEL 1

## Slide 26: PERFORMANCE
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
19 - 21 WINDOWS
3 OPTIONS
18 – 20 WINDOWS
3 OPTIONS
18 – 20 WINDOWS
3 OPTIONS
TOTAL
3X3X3 = 27 OPTIONS

## Slide 27: PERFORMANCE
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
21 WINDOWS
20 WINDOWS
20 WINDOWS
BEST DAYLIGHT OPTION OUT OF THE 27 TOTAL OPTIONS
19 - 21 WINDOWS
18 – 20 WINDOWS
18 – 20 WINDOWS

## Slide 28: CATEGORIZE THE OPTIONS
OPTIONS WITH WINDOWS
OPTIONS WITHOUT WINDOWS

## Slide 29: OPTIONS WITH WINDOWS
21 Options
8 Options
Window At
Level 1 Only
Window At Level 2 Only
9 Options
Window At Level 3 Only
4 Options
Window At Level 1&2
3 Options
Window At Level 1&3
1 Option
Window At Level 1,2&3
2 Options
Window At Level 2&3

## Slide 30: OPTION A
21 Options
8 Options
Window At Level 1 Only
Window At Level 2 Only
9 Options
Window At Level 3 Only
4 Options
Window At Level 1&2
3 Options
Window At Level 1&3
1 Option
Window At Level 1,2&3
2 Options
Window At Level 2&3

## Slide 31: OPTION A | Picking Window Bays
1 Option
Window At Level 1,2&3
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
21 WINDOWS
20 WINDOWS
20 WINDOWS
Pick 1 Out Of 21 Options
Window At Level 1 Only

## Slide 32: OPTION A | PICKING SOLID BAYS
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
21 WINDOWS
20 WINDOWS
20 WINDOWS
21 SOLID
22 SOLID
22 SOLID
Pick 22 Out Of 65 Solid Options
Without Repetition
C(65, 22) = 1.214554453 * 10^17
With Repetitions
P(65, 22) = 1.365160089 * 10^38

## Slide 33: OPTION A – Alternating between window bay and solid bay
21 bays with solid panels
Choosing 21 out of 1.214554453 * 10^17 or 1.365160089 * 10^38
20 bays with windows at all levels
Choosing 1 out 1
4
8
12
16
20
24
28
32
36
40

## Slide 34: OPTION A – Alternating between window bay and solid bay
21 bays with solid panels
Choosing 21 out of 1.214554453 * 10^17 or 1.365160089 * 10^38
20 bays with windows at all levels
Choosing 1 out 1
1 bay with window at Level 1
42 ways to add the one window bay
4
8
12
16
20
24
28
32
36
40
+
random.choice

## Slide 35: OPTION A

## Slide 36: OPTION B
21 Options
8 Options
Window At Level 1 Only
Window At Level 2 Only
9 Options
Window At Level 3 Only
4 Options
Window At Level 1&2
3 Options
Window At Level 1&3
1 Options
Window At Level 1,2&3
2 Options
Window At Level 2&3

## Slide 37: OPTION B
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
21 WINDOWS
20 WINDOWS
20 WINDOWS
Window At Level 2 Only
Window At Level 1&3
Pick 1 Out Of 21 Options
Window At Level 1 Only
Pick 20
Pick 20
1

## Slide 38: OPTION B

## Slide 39: OPTION C
21 Options
8 Options
Window At Level 1 Only
Window At Level 2 Only
9 Options
Window At Level 3 Only
4 Options
Window At Level 1&2
3 Options
Window At Level 1&3
1 Options
Window At Level 1,2&3
2 Options
Window At Level 2&3

## Slide 40: OPTION C
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1
21 WINDOWS
20 WINDOWS
20 WINDOWS
2
1
6
1
6
6
6
6
6
1
1

## Slide 41: OPTION C

## Slide 42
OPTION A
OPTION B
OPTION C

## Slide 43: METHOD 2 - Incremental Analysis
42 VERTICAL BAYS
LEVEL 3
LEVEL 2
LEVEL 1

## Slide 44
7 –bay module
14-bay module
21-bay module
42 Bays X 1
X 2
X 3
X 6

## Slide 45
6-bay module
3-bay module
2-bay module
X 7
X 14
X 21

## Slide 46
6-bay module
3-bay module
2-bay module
X 7
X 14
X 21

## Slide 47: 2-bay Module
2-bay module
X 21
Total of 42 bays
19 - 21 WINDOWS
18 – 20 WINDOWS
18 – 20 WINDOWS
LEVEL 3
LEVEL 2
LEVEL 1
20 WINDOWS
20 WINDOWS
20 WINDOWS
X 20 +
X 2

## Slide 48: 2-bay Module

## Slide 49: 2-bay Module
2-bay module
X 21
Total of 42 bays
19 - 21 WINDOWS
18 – 20 WINDOWS
18 – 20 WINDOWS
LEVEL 3
LEVEL 2
LEVEL 1
20 WINDOWS
20 WINDOWS
20 WINDOWS
X 20 +
X 2
4 types of
2-bay modules

## Slide 50: 2-bay Module

## Slide 51: 2-bay Module Samples
OPTION D
OPTION E

## Slide 52
OPTION A
OPTION B
OPTION C
OPTION D
OPTION E